RI5CY Bare Metal + Testbench tutorial

Summary:

- RI5CY is an in-order 4-stage pipelined RISC-V core with debug unit supporting the RV32IMFCXpulp instruction set and extensions.
- It has a Verilator model and testbench contributed by Embecosm. The testbench instantiates the model and drives it through interactions with the debug unit.
- Code is written directly to memory by the testbench before execution. The core begins execution on reset at address 0x80, the reset vector.

Goal:

- Build a pre-existing model of the RI5CY core and execute instructions on it
- Examine core behaviour with GTKWave

Resources:

- Ri5CY user manual: http://www.pulp-platform.org/wp-content/uploads/2017/11/ri5cy_user_manual.pdf
- RISC-V User-level ISA, version 2.2: https://riscv.org/specifications/

Steps

Obtaining the source

Clone the Ri5CY git repository:

  git clone https://github.com/pulp-platform/riscv.git

Building the model

In the verilator-model subdir, run make:

  cd verilator-model
  make

If you get an error about using the new operator with an over-aligned type, this is because you have a recent GCC C++ compiler. Edit line 23 of the Makefile to add the -faligned-new flag, so it reads:

  CXXFLAGS = -Wall -Werror -std=c++11 -faligned-new

Running the model

The model can be executed by invoking the testbench program:

  ./testbench

Examining execution with GTKWave

Open the trace file with GTKWave:

  gtkwave model.vcd

As RI5CY is a moderately complex design, there are a lot of interesting parts to look at. Some interesting modules and signals include:

- top.riscv_core_i.if_stage_i. The prefetch buffer can be found underneath in genblk1.prefetch_128.prefetch_buffer_i, with the buffer register itself being called instr_rdata_i. Look at this along with the clock signal (clk) to observe the buffer during execution.
- top.riscv_core_i.debug_unit_i. The debug unit, through which the testbench interacts with the core. The debug unit is described on Page 31 of the RI5CY user manual. You examine the signals here to see interactions between the testbench and core. In particular, signals such as dbg_req_o, debug_gnt_o, debug_halt_o, debug_req_i, debug_we_i, debug_addr_i, etc. may be of interest.
- top.riscv_core.load_store_unit_i. This is the core’s interface to the memory. Its protocol is described on page 10 of the RI5CY manual. You should be able to see instructions being fetched from memory here. Signals include data_req_o. data_addr_o, data_we_o, data_be_o, data_wdata_o, data_rdata_i, data_rvalid_i, data_gnt_i.

Modifying instruction code

The loadProgram() function pokes RISC-V instructions into memory. These represent the assembly code:
  li a5, 64
  li a4, 102
  sw a4, 0(a5)

to begin with, then eventually perform the equivalent of the exit system call.

An example of one instruction being written to memory is:

    cpu->top->ram_i->dp_ram_i->writeByte (addr + 0x0, 0x93);
    cpu->top->ram_i->dp_ram_i->writeByte (addr + 0x1, 0x07);
    cpu->top->ram_i->dp_ram_i->writeByte (addr + 0x2, 0x00);
    cpu->top->ram_i->dp_ram_i->writeByte (addr + 0x3, 0x04);

You can change the sequence of instructions placed in memory to execute a different program. This will require either:

- Some understanding of RISC-V assembly to write the opcodes directly
- Use of the RISC-V assembler and objdump tool to convert assembly code into opcodes for entering into the testbench.

You may find going through this process a fun and/or interesting exercise – however, you may instead wish to work on the “Running programs on verilated models through a GDBServer” tutorial to run some different programs on a RISC-V core.

Modifying the instruction prefetch buffer width

The top module has a parameter for controlling the fetch width when reading instructions, INSTR_RDATA_WIDTH:

   module top
  #(
    parameter INSTR_RDATA_WIDTH = 128,
    parameter ADDR_WIDTH = 22,
    parameter BOOT_ADDR = 'h80 // Consistent with Pulpino
  )

This parameterises the RISC-V core further down the file:

  riscv_core
   #(
     .INSTR_RDATA_WIDTH (INSTR_RDATA_WIDTH)
    )
  riscv_core_i
  …

See if you can trace through the code to understand how this eventually parameterises generation of the prefetch buffer in the instruction fetch stage (rtl/riscv_if_stage.sv):

 generate
    if (RDATA_WIDTH == 32) begin : prefetch_32
   …
    end else if (RDATA_WIDTH == 128) begin : prefetch_128
  …

The core supports 32- or 128-bit prefetch buffers.

See if you can modify the top module and dual-ported RAM (dp_ram.sv) to use a 32-bit prefetch buffer. To do this you will need to:

- Change the value of INSTR_RDATA_WIDTH in top.sv
- Change the width of instr_rdata in top.sv
- Modify the width of rdata_a_o in dp_ram.sv
- Modify the always block in dp_ram.sv so that it assigns 32 bits instead of 128 bits to rdata_a_o.

When you rebuild and re-run the testbench, the output should be identical to that produced before any modification is made.

You should be able to see the differences in these modified signals and in the prefetch buffer in GTKWave.