Verilated Counter tutorial

Goal:

Starting from a template:

- Build a verilated model of the counter
- Interact with it using a testbench
- Add functions and tasks to work with internal state
- Dump traces and visualise in GTKWave

Resources:

- Chip hack website
- OSHCamp talk slides

Solution:

A worked solution to this exercise is available in the write_with_task branch of the source repository obtained below.

Steps

Obtaining source:

Clone the template source:

  git clone -b tutorial_start https://github.com/gmarkall/verilated-counter.git

Building:

Run:

  make

In the initial state the build fails because the implementation is incomplete.

Have a look at the file counter.v – try to understand its implementation and how it works.

Completing the top module:

The interface to the module needs completing – it has no inputs and outputs defined:

  module top
  #(
    // Parameter list
   )
  (
    // Port list
    /* Fill in inputs and outputs to module */
  );

We want to expose all of the inputs and outputs of the counter, so our top module needs:

- 3 1-bit inputs for clock, reset, and enable
- 1 8-bit output for the count

The counter is already instantiated, but its inputs and outputs are not connected up:

  counter
   #(
     .CYCLES_PER_COUNT ( 4 )
    )
  counter_i
    (
      /* Connect inputs and outputs of counter to
       * top module inputs and outputs */
    );

Each input and output needs connecting to the corresponding input and output of the top module. Do this for each of them. For example to connect the clock_i input of the counter to the clock wire of our top module:

  .clock_i ( clock ),

Build the model again:

  make

The Verilator run and compilation of the verilated code should complete without error, but the testbench will fail to compile.

Completing the C++ test bench

The C++ testbench (testbench.cpp) already instantiates the model, but it has no implementation of the clockModel() function. The clockModel() function should:

- Set the clock pin to 0
- Call the eval() function of the model
- Set the clock pin to 1
- Call the eval() function again.

Add an implementation of the clockModel() function and rebuild:

  make

You should now be able to run the test bench. At present the model will be driven forward in time, but none of the model state will be outputted.

You can now execute the testbench with:

  ./testbench

Some output will be produced, but none of it represents any of the state in the model.

Displaying the counter output

The outputState() function is a placeholder for printing state:

void outputState()
{
  /* Add code to output state */
}

You can access the counter through model->count. Add some code to print this value out in outputState and recompile. Running the testbench again should display the count in its output.

Accessing the internal counter with a function.

In counter.v, add a function to read the internal counter. A template for a function is:

 function <output width> <name>;
    /* verilator public */
    begin
      <function statements>;
    end
  endfunction

The output width is [7:0], to match the width of the internal counter. In the function body, assign the internal counter value to the function name.

The function can be accessed from C++ through model->top->counter_i-><function name>() - modify the outputState() function so that it also outputs the internal counter value.

Recompile the testbench. When you run it again, you should see both internal and external counter values.

Modifying the internal counter with a task

In counter.v, add a task to write the internal counter. It should take an input of with [7:0] and assign it to internal_count. A template for a task is:

  task <task name>;
    /* verilator public */
    <task inputs>
    begin
      <task statements>;
    end
  endtask

There is a placeholder for calling the task to set the internal counter in the testbench:

  cout << endl << "Setting internal counter to 2..." << endl;

  /* Call task to set internal counter here */

Insert a call to the task here, and make sure to also call the model’s eval() function immediately afterwards. When you rebuild and run the testbench, you should see the effect of the task setting the internal counter towards the end of the output.

A note on modifying state with tasks

When we wrote the task, we used a blocking assignment to write to the internal counter:

  internal_count = new_internal_count;

However, there are non-blocking (or delayed) assignments to the internal count inside the implementation of the counter:

  always @(posedge clock_i) begin
    if (reset_i) begin
      count_o <= 0;
      internal_count <= 0;
    end else if (enable_i) begin
      if (internal_count == (CYCLES_PER_COUNT - 1)) begin
        count_o <= count_o + 1;
        internal_count <= 0;
      end else
        internal_count <= internal_count + 1;
    end

This usually causes an issue when we generate the model with Verilator:

%Error-BLKANDNBLK: counter.v:14: Unsupported: Blocked and non-blocking assignments to same variable: internal_count
%Error: Exiting due to 1 error(s)
%Error: See the manual and http://www.veripool.org/verilator for more assistance.
%Error: Command Failed /usr/bin/verilator_bin top.v counter.v --top-module top --cc --trace

Usually Verilator doesn’t support both a blocking and non-blocking assignment in general. However, for the purpose of only using a blocking assignment inside a task called from a C++ testbench, it works correctly, as long as. In order to work around this error, we add an extra flag when we invoke Verilator:

  verilator -Wno-BLKANDNBLK <other arguments>

See also: https://www.veripool.org/issues/449-Verilator-Using-public-accessor-tasks-functions-to-read-and-write-registers-causes-BLKANDNBLK-error for more information.

Dumping state in trace files

There is a placeholder for instantiating the trace file in the testbench:

  model = new Vtop;
  /* Instantiate trace file here */

as well as one for its close:

  /* Close the tracefile here */

In the placeholder for instantiating the tracefile, we need to:

  traceFile = new VerilatedVcdC; // Instantiate an object for tracing
  model->trace(traceFile, 99); // Connect our model with the trace file
  traceFile->open("model.vcd"); // Open a file on disk for dumping to

In the placeholder for closing, we need to add:

  traceFile->close();

We also need to dump state to the tracefile. We can do this at every clock edge. Modify the clockModel() function so that after each call to eval():

- simTime is increased by 5.
- traceFile->dump(simTime) is called.

Rebuild the model and run the testbench again. There should be a new file in the output directory, called model.vcd.

Inspection with GTKWave

Open the trace file with GTKWave:

  gtkwave model.vcd

Notes on using GTKWave:

- The top left pane is for navigating the structure of the Verilog
- When a Verilog module is highlighted, the bottom left pane shows the signals in that module.
- Signals of interest can be dragged into the list of signals on the right-hand pane.
- Zooming in and out (+ and – icons on the toolbar) can be helpful for examining model behaviour at the right level of detail.